## Slide 1
WhisperComm: A Modern Communication Project
AI-Driven Speech Enhancement for AM Signals in Degraded Channels

## Slide 2: PROBLEM & OBJECTIVES
Problem AM voice communications, though simple and widely used in aviation and maritime systems, degrade severely under noise. Traditional filters distort speech and fail under non-stationary conditions, making speech unintelligible for both humans and automated systems.
Objectives
Simulate a complete AM channel with realistic noise.
Apply state-of-the-art AI denoiser for post-demodulation enhancement.
Validate improvements objectively via Whisper ASR Word Error Rate (WER).

## Slide 3: THE THREE PILLARS
Software-Defined Radio (SDR): Building radios in software rather than circuits.
1
Signal-to-Noise Ratio (SNR): The universal measure of signal quality against noise.
2
Artificial Intelligence (AI): Intelligent denoising and transcription for speech recovery.
3

## Slide 4: METHODOLOGY OVERVIEW
Load clean speech (ground truth).
Modulate with 4 kHz carrier.
Inject pink noise at different SNR levels.
Demodulate using envelope detection (rectifier + low-pass).
Enhance with AI denoiser.
Evaluate intelligibility using Whisper ASR.

## Slide 5: SIGNAL PROCESSING WORKFLOW
AM Modulation: generates the carrier-modulated signal.
Noise Generation: Pink noise synthesized via spectral shaping to reflect real-world interference.
Channel Simulation: Noise power adjusted to achieve exact SNR levels.
Demodulation:
  Rectifier:
  Low-pass filter (Butterworth, 3800 Hz cutoff) extracts envelope.
Result: A noisy baseline audio stream resembling real degraded AM speech.

## Slide 6: IMPLEMENTATION SETUP
Software Environment:
Python 3 with Colab Notebook for modular, interactive workflow.
Core Libraries:
PyTorch: Loads pretrained AI denoiser.
Transformers/Datasets: Provides Whisper ASR and Librispeech source.
SciPy: Filtering and signal design.
Librosa: Visualization of speech waveforms and spectrograms.
NumPy: Core numerical computations.

## Slide 7: AI MODELS USED
1. Speech Enhancement (DNS64):
Loaded via PyTorch, pretrained on massive noisy-clean datasets.
Likely U-Net/CRN architecture.
Function: Removes noise while preserving formant structures critical for intelligibility.
2. ASR Model (Whisper-large-v3):
Hugely robust ASR trained on 680k hours of audio.
Evaluates transcription accuracy before/after enhancement.
Metric: Word Error Rate (WER).

## Slide 8: SIMULATION CODE SNIPPET
Core AI Enhancement Pipeline (PyTorch):
Convert noisy NumPy audio → PyTorch tensor.
Use torch.no_grad() to run inference efficiently.
Pass through DNS64 denoiser → obtain enhanced tensor.
Convert tensor back to NumPy for playback and evaluation.
This concise, GPU-accelerated pipeline makes AI enhancement real-time capable while ensuring reproducibility in academic and industrial contexts.

## Slide 9: SPECTROGRAM EVIDENCE (NOISY)
At 12 dB SNR, the noisy baseline signal shows heavy corruption:
Clean speech spectrogram: Distinct formants and harmonic bands visible.
Noisy demodulated spectrogram: Broadband noise floor masks details, blurring speech cues.
The visual confirms why AM under noise is unintelligible and why traditional filters fail—non-stationary noise disrupts speech structure beyond recovery.

## Slide 10: SPECTROGRAM EVIDENCE (ENHANCED)
AI Enhancement restores intelligibility at 12 dB SNR:
Noisy baseline: Dense noise obscures speech bands.
AI-enhanced spectrogram: Noise floor removed, dark background restored.
Clear formants and harmonics emerge, resembling clean reference.
This validates the AI denoiser’s learned capability to separate human speech features from disruptive noise patterns.

## Slide 11: IMPLICATIONS & LIMITATIONS
Implications:
Revives legacy AM systems for modern automation.
Enables archival transcription of historical, noisy audio.
Increases safety in aviation, maritime, and emergency voice communications.
Limitations:
Pure simulation; no real-air recordings used.
Only pink noise tested; real-world multipath/fading unmodeled.
No subjective human evaluation (MOS, MUSHRA).

## Slide 12: CONCLUSION & FUTURE WORK
Conclusion: The project proves AI-based denoising as a transformative solution for noisy AM speech, restoring intelligibility and enabling accurate ASR transcription across degraded channels.
Future Work:
  Validate with real-world AM recordings.
  Test broader languages, speakers, and noise types.
  Include subjective quality tests (MOS, listening panels).
  Optimize AI for real-time deployment on embedded systems.